Tigress Chamber tuning & alignment

(Apr. 6/14 - TA)

*assumes beam tuned to SEBT:FC20; current monitor system set up & event handler open

Perform rad survey (gamma/neutrons) when beam initially sent into ISAC-II Experimental hall & again after tuning at full intensity & maximum energy.

Load theory from ISAC2 spreadsheet for SEBT:FC20-SEBT3A:FC4.

Tune to SEBT3A:FC4 using SEBT:YCB22, MB22; SEBT3:MB4 & YCB4.

Tune through blank aperture using SEBT3A:(X/Y)CB2, SEBT3:MB4 & YCB4.

Tune through 2mm collimator using SEBT3A:(X/Y)CB2, SEBT3:MB4 & YCB4, SEBT3A:Q1-4 (& if desperate, SEBT:Q17-20); ~80%+ Tx is expected, 70% might be accepted depending on the exp't.

In general, all SEBT steerers from SEBT:XCB18 on and both dipoles; no quads until 2mm alignment & then only SEBT3A:Q1-4 & SEBT:Q17-20 if desperate (preferably none in between).