TRIUMF Memo	Date: May 30, 2011

To:	Reiner Kruecken; Gordon Ball

From:	Joe Mildenberger

RE:	Actinide Target Experiments and Safety; Yield station measurements

N.b. This memo condenses and summarizes several earlier memos and emails I had sent to Gordon Ball regarding recommendations for standard safety precautions to be taken for yield measurements in general, and also particular safety measures required due to hazards associated with running actinide targets. Gordon had requested that these instructions be combined into a single memo that could be referenced in experimental safety reports and completion documents.

Although I encourage people to whom these instructions are relevant to familiarize themselves with the details presented below, I can summarize the key points very briefly:

Yield measurements:
- A 3m exclusion zone around the yield station should be flagged off prior to starting measurements.
- If it is intended to extract low-mass neutron emitters: Because the ISAC-I experimental hall has no neutron monitors, if it is planned to bring up nuclides which decay via neutron emission a portable neutron detector (“Snoopy”) should be obtained from the RPG, and its scaler output fed into the EPICS system so as to be available to experimenters and Operators.

Detector openings during and after actinide target operations
The RPG should be consulted prior to any initial detector openings during or following the delivery of beam from actinide targets. This is already a requirement for “normal” openings, but is emphasized in this context due to the increased hazards associated with alpha-emitting nuclides which may be present.

 These items should be considered “Standard Operating Procedure” for yield measurements, and for detector or beamline openings where lingering hazards from actinide target operations are a concern. The detailed considerations follow.

Yield station measurement protocol:

Regarding the long list of nuclides proposed for the yield station measurements:
I think we've been through the process enough times that we are probably in general agreement about the sensible way to proceed to avoid problems associated with external dose rates around the yield station that could potentially trip the beam off. My somewhat wordy email of 2009-06-05 contains the essence of my advice in this area, much of which is and was the established practice for yield measurements anyway:

     After speaking with Marik, and considering the length of the list of nuclides, I came to the conclusion that the uncertainties on the expected yields and on the amount of shielding we should expect from the yield station, would make dose rate calculations essentially useless for providing specific advice.
     So, what I am going to recommend it that we compensate for our ignorance by creating a 3m exclusion zone around the yield station. The most immediately obvious result of doing this is that Anne's list of "safe" levels for different decay modes immediately increases by 2 orders of magnitude uniformly, assuming no shielding.
     Next, taking into account the construction of the yield station, which looks to me to be 1/2" slabs of steel and copper, and taking into account the lead bricks inside which provide significantly more shielding at the bottom, I will then assert that even high-energy betas (some with endpoint energies of up to ~16 MeV) should not be a significant issue. Because the deposition point is near the bottom, there is almost complete shielding of the lower hemisphere of solid angle by two or three inches of lead (at normal incidence; more at angles pointing toward the 3m perimieter), in addition to the steel or copper. Thus, we should also expect significant reduction in gamma dose rate compared with the unshielded values, probably at least another order of magnitude, as one expects roughly a factor of two attenuation for each cm of Pb, for gammas in the 100 keV to several MeV range.
     Neutrons are a bit more problematic, in part due to there being no fixed neutron monitors in the experimental hall. Another aspect of the problem is that the neutron emitters on the list tend to be short lived, while the nature of neutron survey meters ("Snoopies") is that they tend to be slow to react. But I think it is still important to try to measure what we can of them. What I am proposing is that we use the scaler output spigot on the Snoopy to count them on scaler display visible where the experimenters will be. (We did this during the actinide target test.) While we can't measure a dose rate from a short blast of neutron emitters brought up to the yield station, we can measure an integrated dose in this way. Roughly speaking, about 700 counts will correspond to 1 uSv of dose. I am proposing that we put the Snoopy at the 3m perimeter to verify that the potential neutron doses at this distance are within our acceptable limits. I am reasonably confident that the short lifetimes of the neutron emitters will render acceptably small total neutron doses to any0one in the vicinity of the yield station.
     Next, I will suggest proceeding in what I understand from Marik is already the standard m.o. for yield measurements where the error bars on the expected yields are large, which is to start with short collection times for your favourite "benchmark" nuclides, look at what the yields and dose rates do, and then bootstrap from there in a sensible manner. (Given the uncertainties, this would have been my bottom-line recommendation anyway, even if we had a complete set of dose rate predictions for every nuclide on the list...)

Safety Considerations for operations with actinide targets

The other important considerations concern potential internal hazards should a detector need to be opened up during or shortly after actinide target operations, and also the potential for lingering hazards (both external and internal) due to long-lived nuclides.
Regarding immediate internal hazards: During last year's test run with UO2#1 we had occasion to open up the yield station mid-run due to the need to replace a broken tape. Partly as a result of that experience, we believe that we (RPG) have a good, conservatively-safe protocol for dealing with this possibility, which we will use again this year should the need arise. Our only "special request" in this respect is that any such unplanned opening *not* occur prior to consultation with the RPG. It will be sufficient to contact any of the surveyors to attend vacuum system accesses, as they are all up to speed on what needs to be checked. So that instruction should be changed to "Contact RPG before accessing the vacuum system".